## Slide 1
Inference Efficiency
Teacher vs Student
Parameters · FLOPs · Latency · Throughput · Memory
Teacher — ViT-Base (86M)
Student — ViT-Tiny (5.6M)

## Slide 2
Model size — parameters, FLOPs, and disk footprint
15.2×
fewer parameters
15.6×
fewer FLOPs
(16.87G → 1.08G)
15.2×
smaller on disk
(344 MB → 23 MB)
10.2×
less GPU memory
(361.7 → 35.6 MB)
Metric
Teacher (ViT-Base)
Student (ViT-Tiny)
Ratio
Parameters
86.0M
5.6M
15.2×
FLOPs (BS=1)
16.87G
1.08G
15.6×
Disk size
344 MB
23 MB
15.2×
GPU memory
361.7 MB
35.6 MB
10.2×

## Slide 3
Inference latency — single image and small batch
Batch size = 1
Teacher mean
7.12 ms
Student mean
6.45 ms
Speedup
1.1×
Teacher p95
7.69 ms
Student p95
8.58 ms
Teacher tput
140.6 img/s
Student tput
155.2 img/s
Near-identical at BS=1 — both ~7ms on GPU
Batch size = 8
Teacher mean
38.34 ms
Student mean
6.87 ms
Speedup
5.6×
Teacher p95
39.03 ms
Student p95
8.63 ms
Teacher tput
208.6 img/s
Student tput
1,164.9 img/s
Diverges fast — student handles parallel batches far better
Why BS=1 latencies are close but BS=8+ diverges sharply
At BS=1, both models are GPU-bound by kernel launch overhead and memory transfer — the size difference is masked. As batch size grows, the teacher's 16× higher compute per image compounds: 86M parameters × 8 images = 14.5× more arithmetic than the student, and the GPU cannot hide it. The student's 1.08G FLOPs per image scales efficiently; the teacher's 16.87G does not.

## Slide 4
Throughput scaling — images per second across batch sizes
Chart: 
| BS=1 | BS=8 | BS=32 | BS=64
Teacher (ViT-Base) | 140.6 | 208.6 | 207.5 | 157.8
Student (ViT-Tiny) | 155.2 | 1164.9 | 1341.7 | 1404.2
1.1×
speedup at BS=1
(near-identical)
5.6×
faster at BS=8
(student advantage emerges)
6.5×
faster at BS=32
(1,342 vs 208 img/s)
8.9×
faster at BS=64
(1,404 vs 158 img/s)

## Slide 5
Latency percentiles — mean, p50, p95, p99 across batch sizes
Model
BS
Mean
p50
p95
p99
Throughput
Teacher
1
7.12ms
7.01ms
7.69ms
8.37ms
140.6 img/s
Student
1
6.45ms
6.15ms
8.58ms
9.45ms
155.2 img/s
Teacher
8
38.34ms
38.38ms
39.03ms
39.38ms
208.6 img/s
Student
8
6.87ms
6.77ms
8.63ms
9.94ms
1,164.9 img/s
Teacher
32
154.2ms
149.4ms
166.6ms
171.6ms
207.5 img/s
Student
32
23.85ms
23.82ms
24.16ms
25.18ms
1,341.7 img/s
Teacher
64
405.5ms
409.3ms
453.5ms
467.0ms
157.8 img/s
Student
64
45.58ms
45.32ms
47.12ms
49.17ms
1,404.2 img/s

## Slide 6
Key findings
1
15× compression with minimal latency penalty at BS=1 (7.12ms → 6.45ms, effectively identical). The teacher's parameter advantage does not translate to single-image speed due to GPU kernel overhead.
2
Throughput diverges dramatically at scale: 8.9× more images/second at BS=64 (1,404 vs 158 img/s). The student's 1.08G FLOPs per image scales efficiently as batches grow; the teacher's 16.87G does not.
3
10× less GPU memory (35.6 MB vs 361.7 MB). The student fits comfortably on edge GPU budgets where the teacher would not — a critical advantage for deployment.
4
15× smaller on disk (23 MB vs 344 MB) makes the student practical for mobile deployment, model serving, and over-the-air updates.